## Slide 1: GCSE Additional Revision Sessions Easter 2026
8+ Mark Exam Question Techniques

## Slide 2: Extended Question – 6 Step Strategy
Read the question thoroughly - and any pre-ceding elements of the question in full.
Analyse what is being asked.
  Box or highlight the command word(s) – consider what they mean
  Circle the marks available
  Underline the topic and question context
Break the question down – establish how many separate parts need to be written for a full mark answer.
Plan your answer – write a plan for each paragraph.
Write your answer – Try to do this carefully so it is tidy and coherent.
Check your answer – read through your answer, making any adjustments or additions if necessary.

## Slide 3: Example Number 1
Walk through example

## Slide 4: Step 1 – Read the question thoroughly
1 (c)
Susan needs to email her coursework from her home computer to her school sever. Explain how packet switching works to manage this transfer. Your explanation should start when Susan presses send and should finish with the email is received on the school server.
(The quality of your written communication is assessed in this question).
8 Marks

## Slide 5: Step 1 – Read the question thoroughly
1 (c)
Susan needs to email her coursework from her home computer to her school sever. Explain how packet switching works to manage this transfer. Your explanation should start when Susan presses send and should finish with the email is received on the school server.
(The quality of your written communication is assessed in this question).
8 Marks
But also: additional introduction to the question a few pages ahead in the paper
A school uses a local area network (LAN) to connect together all its computing devices. The network manager is able to identify each device on the network by both an IP address and MAC address.

## Slide 6: Step 2 – Analyse what is being asked
1 (c)
Susan needs to email her coursework from her home computer to her school sever. Explain how packet switching works to manage this transfer. Your explanation should start when Susan presses send and should finish with the email is received on the school server.
(The quality of your written communication is assessed in this question).
8 Marks
But also: additional introduction to the question a few pages ahead in the paper
A school uses a local area network (LAN) to connect together all its computing devices. The network manager is able to identify each device on the network by both an IP address and MAC address.

## Slide 7: Step 2 – Understanding the command words
Explain - To give account of the purposes or reasons. Make them clear to the reader.
1 (c)
Susan needs to email her coursework from her home computer to her school sever. Explain how packet switching works to manage this transfer. Your explanation should start when Susan presses send and should finish with the email is received on the school server.
(The quality of your written communication is assessed in this question).
8 Marks

## Slide 8: Step 3 – Break down the question
Part 1 – Introduction and general explanation that sending the email with make use of the internet which is a packet switched network (No specific marks allocated but important for the context / application of the answer)
  Make clear that by sending an email from a personal computer to the school server the process of packet switching will be used. May include a very brief general description of what that means.
Part 2 – Explain in context of this email, as many technical points as possible about what happens during the sending process in a packet switched network (Approx 3 – 4 marks)
  Make clear each of the most important things that happen when the email is in the sending phase of the data transmission
Part 3 – Explain in context of this email, as many technical points as possible about what happens during the transmission process in a packet switched network (Approx 1 – 2 marks)
  Make clear each of the most important things that happen when the email is in the transmission phase of the data transmission
Part 4 – Explain in context of this email, as many technical points as possible about what happens during the receiving process in a packet switched network (Approx 3 – 4 marks)
  Make clear each of the most important things that happen when the email is in the receiving phase of the data transmission
Susan needs to email her coursework from her home computer to her school sever. Explain how packet switching works to manage this transfer. Your explanation should start when Susan presses send and should finish with the email is received on the school server.
(The quality of your written communication is assessed in this question).
8 Marks

## Slide 9: Step 4 – Plan the answer
Make clear that by sending an email from a personal computer to the school server the process of packet switching will be used. May include a very brief general description of what that means. Paragraph 1 | Explain that by sending an email from her home computer to the school server, the data will need to be sent through the internet. The internet is a packet switched network; therefore, the data content of the email and the attached coursework will be subject to the process of packet switching during the sending, transmission and receiving of the email Explain briefly that this means that the data will be broken down into smaller sections of data called packets and each transported on its own, potentially different route in order to reach the destination.
Make clear each of the most important things that happen when the email is in the sending phase of the data transmission Paragraph 2 | The email and the coursework attachment are broken down into equal sized groups of data called packets Each packet contains it’s own data but is also allocated a header which contains important data for the packet switching process The header includes the packet sequence number to allow it to be reassembled in order The source address of the sending computer The destination address of the school server it is to be sent to Error checking and correction data, allows packets to be checked to see if they have become corrupt Packets are sent from her own computer, through her home router and out to the internet
Make clear each of the most important things that happen when the email is in the transmission phase of the data transmission Paragraph 3 | Each individual packet may take a different path to reach the destination When the packet reaches a node, it will be directed to the next node in sequence depending on the least congested possible route This changes very quickly and so may result in packets being sent through different nodes on their route to the destination This will likely result in packets being sent to the destination via different routes
Make clear each of the most important things that happen when the email is in the receiving phase of the data transmission Paragraph 4 | The school server receives packets in the order that they arrive The sequence number on each packet is used to re-order the email and coursework attachment If any of the packets have not arrived in a given time frame the server will request that these packets are re-sent The error checking information is checked to see if any packets are corrupt If there are corrupt packets they are also requested to be re-sent my the server Once complete and re-assembled the server sends a confirmation of receipt to Susan’s computer

## Slide 10: Step 5 – Write the answer – paragraph 1
If Susan sends her coursework via email, from her home computer to the school server, she will need to use the internet to do so. The internet is a packet switched network, therefore the data in the email and the attached coursework will be subject to the process of packet switching in-order to reach its destination. In short this means the data will be broken down into smaller sections with each being send across the most appropriate pathway at any given time, to reach the intended destination.

## Slide 11: Step 5 – Write the answer – paragraph 2
The first thing to happen in the sending process by Susan’s computer is that the email and the coursework attachment will be broken down into equal sized groups of data called data packets. Each packet contains its own data but is also allocated a header which contains important data for the packet switching process. The header includes:
the packet sequence number to allow it to be reassembled in order,
the source address of the sending computer
the destination address of the school server it is to be sent to
error checking and correction data, allows packets to be checked to see if they have become corrupt
The packets are then sent from her own computer, through her home router and out to the internet.

## Slide 12: Step 5 – Write the answer – paragraph 3
In transit through the internet, each individual packet may take a different path to reach the destination. This happens because when the packet reaches a node; it will be directed to the next node in sequence depending on the least congested possible route. This changes very quickly and so may result in packets being sent through different nodes on their route to the destination. This will likely result in packets being sent to the destination via different routes, but ensures the most efficient transmission of data, by not allowing data packets to be held up by congested areas of the network.

## Slide 13: Step 5 – Write the answer – paragraph 4
The school server receives the data packets in the order that they arrive, which may not be in order. The sequence number on each packet header is used to re-order the email and coursework attachment. If any of the packets have not arrived in an agreed time frame the server will request that these packets are re-sent. Each packet is checked for errors using the error checking information to see if they have become corrupt in-transit. If there are ant corrupt packets, they are also requested to be re-sent by the server. Once all packets have been received and re-assembled the transmission is complete and the server sends a confirmation of receipt to Susan’s computer.

## Slide 14: Step 6 – Check your answer
Mark Scheme
Higher level Response (7-8)
Reasoned response. Candidate clearly breaks down explanation into both sending and receiving. The response is constructed well and reads like a sensible journey. Points well made. Few if any SPAG issues. Technical terms used correctly
Medium level Response (4-6)
Candidate describe the steps. Attempts have been made to cover some points for both sending and receiving. The answer might feel a little disjointed in places. Most points well made. Occasional errors in SPAG. Technical terms will have been used correctly on the whole.
Low level Response (1-3)
Points made are purely identified. They are not followed up with descriptions or explanations. Various separate points are rarely linked together. On the whole information presented isn’t expressed very well and the discussion is limited. One or both sides (Sending / Receiving) might be weak or omitted entirely. Few technical terms will have been used / used correctly. Errors in SPAG may be intrusive.

## Slide 15: Step 6 – Check your answer
Mark Scheme
Technical points to make.
Points to make for “Sending”:
Email is split into packets (1) of equal size (1), Each packet is numbered in sequence (1) e.g. 1 of 8, Each packet is given the source address of Susan’s computer (1), Each packet is given the destination address of the school server (1), Each packet has error checking data / information added (1), Each packet is sent out from Susan’s computer over her home network (1) and out onto the Internet
Points to make for “In-Transit”:
When each packet reaches a new node on its way to the destination it is directed onwards depending on the path of least traffic (1), This can result in packets arriving at the destination out of sequence (1)
Points to make for “Receiving”:
The school server requests the resending of any packets which “time out” (don’t arrive in a given time frame (1), The school server reorders the packets into their correct sequence (1), Each packet is checked for errors (1), If errors / corrupt packets found request is sent to Susan’s computer to resend that packet (1), The school server sends a “confirmation of receipt” to Susan’s computer (1)

## Slide 16: Example Number 2
Scaffolded example

## Slide 17: Step 1 – Read the question thoroughly
2.
“Up 2 Learn” is a new start up company offering a cloud based online virtual learning environment for schools. The “Up 2 Learn” website software will allow students to share ideas, files, documents and access discussion rooms and forums. Each student will have their own account to log in to the learning environment.
(a)
Discuss the various legal and ethical issues “Up 2 Learn” will have to consider when creating their virtual learning website.
(The quality of you written communication is assessed in this question).
8 Marks

## Slide 18: Step 2 – Analyse what is being asked
2.
“Up 2 Learn” is a new start up company offering a cloud based online virtual learning environment for schools. The “Up 2 Learn” website software will allow students to share ideas, files, documents and access discussion rooms and forums. Each student will have their own account to log in to the learning environment.
(a)
Discuss the various legal and ethical issues “Up 2 Learn” will have to consider when creating their virtual learning website.
(The quality of you written communication is assessed in this question).
8 Marks

## Slide 19: Step 2 – Understanding the command words
Discuss - Give an account that addresses a range of ideas and arguments
2.
“Up 2 Learn” is a new start up company offering a cloud based online virtual learning environment for schools. The “Up 2 Learn” website software will allow students to share ideas, files, documents and access discussion rooms and forums. Each student will have their own account to log in to the learning environment.
(a)
Discuss the various legal and ethical issues “Up 2 Learn” will have to consider when creating their virtual learning website.
(The quality of you written communication is assessed in this question).
8 Marks

## Slide 20: Step 3 – Break down the question
Part 1 – Discussion of the laws that need to be considered (Approx 4 marks)
  A discussion of how they will have to consider the DPA clearly contextualised to the VLE
  A discussion of how they will have to consider the CMA clearly contextualised to the VLE
  A discussion of how they will have to consider the CDPA clearly contextualised to the VLE
Part 2 – Discuss ethical issues that need to be considered (Approx 4 marks)
  Suggest 3-4 ethical concerns the company will need to consider, make sure these are applicable to the context of the VLE
“Up 2 Learn” is a new start up company offering a cloud based online virtual learning environment for schools. The “Up 2 Learn” website software will allow students to share ideas, files, documents and access discussion rooms and forums. Each student will have their own account to log in to the learning environment.
(a)
Discuss the various legal and ethical issues “Up 2 Learn” will have to consider when creating their virtual learning website.
(The quality of you written communication is assessed in this question).
8 Marks

## Slide 21: Step 4 – Plan the answer
An introductory paragraph giving context. Paragraph 1 | 
A discussion of how they will have to consider the DPA clearly contextualised to the VLE Paragraph 2 | 
A discussion of how they will have to consider the CMA clearly contextualised to the VLE Paragraph 3 | 
A discussion of how they will have to consider the CDPA clearly contextualised to the VLE Paragraph 4 | 
Suggest 3-4 ethical concerns the company will need to consider, make sure these are applicable to the context of the VLE Paragraph 4 | 

## Slide 22: Step 4 – Plan the answer
An introductory paragraph giving context. Paragraph 1 | Introduce the answer, make it clear that as the company are online and will be dealing with a large number of students and their data that they will have to consider each of the laws in order to make sure they are operating legally Also explain that in order to set the correct example and keep the students safe they should consider a number of ethical concerns
A discussion of how they will have to consider the DPA clearly contextualised to the VLE Paragraph 2 | Must comply with the principles of the DPA ( only need to mention 2-3 of these but must be in context of the school and VLE) Students' data to be collected and processed lawfully and fairly Limited only to the purposes stated which is to support their education Only collect relevant information / not permitted to collect excessive data not relevant to their education Must be accurate and up to date Kept no longer than necessary – removed after students leave the school or stop using the platform Processed in-line with their rights Data must be kept secure – use of encryption and firewalls Should only be stored in UK data centres or countries which offer adequate data protection laws
A discussion of how they will have to consider the CMA clearly contextualised to the VLE Paragraph 3 | Data should only be accessible to those with appropriate access rights, require usernames and passwords to do so Appropriate security measures taken to protect the data against unlawful access and malware
A discussion of how they will have to consider the CDPA clearly contextualised to the VLE Paragraph 4 | Must make sure that students work is protected from plagiarism, including from each other Must be vigilant of intellectual property rights to make sure that they or the students using the platform do not breach copyright laws
Suggest 3-4 ethical concerns the company will need to consider, make sure these are applicable to the context of the VLE Paragraph 4 | Lega and ethical issues include copying / plagiarising work and the storage of data, particularly that of minors and their parents, must be kept securely There may be e-safety or cyberbullying concerns, company must be adequately prepared to investigate issues where appropriate The needs to be policies developed around acceptable use to keep all users safe All communications and material on the platform should be appropriate for the school and learning environment Attempt to ensure fair access, need to take steps to make sure that not only students with access to the latest technology can access the platform, accessible on a range of devices including older and less powerful devices

## Slide 23: Step 5 – Write the answer:

## Slide 24: Step 5 – Check your answer – Mark Scheme
Mark Scheme
Higher level Response (7-8)
Reasoned response. Detail discussion of both legal and ethical issues. Clearly linked explanations with the scenario. The response is constructed well and reads well. Points well made. Few if any SPAG issues. Technical terms used correctly
Medium level Response (4-6)
Reasonable response. Description of some ethical and / or legal issues. Most points made are explained / justified, though not all will be linked in the context of the scenario. The answer might feel a little disjointed in places. Most points well made. Occasional errors in SPAG. Technical terms will have been used correctly on the whole.
Low level Response (1-3)
Points made are purely identified. They are not followed up with descriptions or explanations. Various separate points are rarely linked together. On the whole information presented isn’t expressed very well and the discussion is limited. One or both sides (legal / ethical) might be weak or omitted entirely. Few technical terms will have been used / used correctly. Errors in SPAG may be intrusive.

## Slide 25: Step 5 – Check your answer – Mark Scheme
Technical points to make.
Points to make for “Legal”:
Data Protection Act (DPA) (1)
Various rules of the DPA as long as they are mentioned in context of scenario: Students data fairly & lawfully processed (1), Students data processed for limited purposes of supporting their education (1), Only relevant / non excessive data held on students (1) e.g. Name, age, school, year group etc. Students data accurate and up to date (1), Students data not kept longer than necessary (1) e.g. 12 months after they leave, Students data processed in line with their rights (1), Students data kept secure (1) e.g. use of firewalls, virus checkers (1), Students data stored in UK data centres (1)
CMA
Any mention of restricting access to the data / logins / usernames / passwords (1)
Copyright, Designs and Patents Act (1)
Mentions of protecting copyright of students and others work (1) / intellectual property considerations (1) or issues with software licences (1)
Points to make for “Ethical”:
Students copying each other’s work / plagiarism (1), Storing information / work / data on minors / parental consent (1), E-safety issues / concerns (1), Acceptable usage policy (1), Issues around cyberbullying / preventing / dealing with the consequences and misuse of the system (1), Inappropriate communication / inappropriate materials via the platform (1), Potential issues about unfair access / unfair advantage to students who have more / better access to technology / the Internet than others (1)

## Slide 26: Example Number 3
Less scaffolded example

## Slide 27: Step 1 – Read the question thoroughly
*Social networking websites use artificial intelligence (Al) to monitor posts from users.
Discuss the positive and negative uses of Al by social networking websites including:
• Legal issues
• Ethical issues
• Privacy issues
8 Marks

## Slide 28: Step 2 – Analyse what is being asked
*Social networking websites use artificial intelligence (Al) to monitor posts from users.
Discuss the positive and negative uses of Al by social networking websites including:
• Legal issues
• Ethical issues
• Privacy issues
8 Marks

## Slide 29: Step 2 – Understanding the command words
Discuss -
*Social networking websites use artificial intelligence (Al) to monitor posts from users.
Discuss the positive and negative uses of Al by social networking websites including:
• Legal issues
• Ethical issues
• Privacy issues
8 Marks

## Slide 30: Step 2 – Understanding the command words
Discuss – Give an account that addresses a range of ideas and arguments
*Social networking websites use artificial intelligence (Al) to monitor posts from users.
Discuss the positive and negative uses of Al by social networking websites including:
• Legal issues
• Ethical issues
• Privacy issues
8 Marks

## Slide 31: Step 3 – Break down the question
Part 1 –
Part 2 –
Part 3 –
Part 4 –
*Social networking websites use artificial intelligence (Al) to monitor posts from users.
Discuss the positive and negative uses of Al by social networking websites including:
• Legal issues
• Ethical issues
• Privacy issues
8 Marks

## Slide 32: Step 4 – Plan the answer

## Slide 33: Step 5 – Write the answer:

## Slide 34: Step 6 – Check your answer – Mark Scheme
Answer: Mark Band 3–High Level (6-8 marks)
The candidate demonstrates a thorough knowledge and understanding of a wide range of considerations in relation to the question; the material is generally accurate and detailed. The candidate is able to apply their knowledge and understanding directly and consistently to the context provided. Evidence / examples will be explicitly relevant to the explanation. The candidate is able to weigh up both sides of the discussion and includes reference to the impact on all areas showing thorough recognition of influencing factors. There is a well-developed line of reasoning which is clear and logically structured. The information presented is relevant and substantiated.
Mark Band 2-Mid Level (3-5 marks)
The candidate demonstrates reasonable knowledge and understanding of a range of considerations in relation to the question; the material is generally accurate but at times underdeveloped. The candidate is able to apply their knowledge and understanding directly to the context provided although one or two opportunities are missed. Evidence/examples are for the most part implicitly relevant to the explanation. The candidate makes a reasonable attempt to discuss the impact on most areas, showing reasonable recognition of influencing factors. There is a line of reasoning presented with some structure. The information presented is in the most part relevant and supported by some evidence.
Mark Band 1-Low Level (1-2 marks)
The candidate demonstrates a basic knowledge of considerations with limited understanding shown; the material is basic and contains some inaccuracies. The candidate makes a limited attempt to apply acquired knowledge and understanding to the context provided. The candidate provides nothing more than an unsupported assertion. The information is basic and communicated in an unstructured way. The information is supported by limited evidence and the relationship to the evidence may not be clear.
0 marks
No attempt to answer the question or response is not worthy of credit

## Slide 35: Step 5 – Check your answer – Mark Scheme
Indicative Content:
Legal issues:
Copyright designs and patents act - can check for plagiarism automatically and highlight posts e.g. videos or images
Data protection act - needs to make sure rules are followed so that the AI algorithm does not breach e.g. security
Check that materials are all legal
User has agreed the terms when signing up so should expect it
Ethical issues:
Users may not want everything they post monitoring
May incorrectly block users/posts
Can limit plagiarism
Can make sure inappropriate/illegal posts are not published
Website will need to tell users what it is doing and they must agree with it
Record of monitoring reports may be stored and used for other means
Users may feel safer using the website because they know inappropriate material will not be published
Privacy issues:
Users may feel like they are being watched all the time
Terms and conditions may sign away their rights to privacy when using the website
People may prefer a computer analysing their posts than people reading them